## Slide 1: Introduction to AI implementation in FPGA via VITIA-AI
(Wed) 27.01.2021
Colloquium at University of Seoul, Dept. of Physics
Sunyoung Yoo

## Slide 2: Little About myself
MSc in Physics at University of Seoul
Training Program for Robotics of KAR
(Korea Association of Robot Industry)
Research Assistant at SDU
MMMI, AI and Data Science Lab

## Slide 3: TABLE OF CONTENTS Ai Model training 03 Capsule Colon Endoscopy CCE project 02 FPGA 01
What and Why
About the project
Object Detection Model Training
with Tensorflow
*tutorial

## Slide 4: TABLE OF CONTENTS ZYNQ, ZCU-102/104 04 VITIA-AI, AI Implementation 05 demo 06
Hardware
Information
How to implement trained model in FPGA via Vitis-AI
From image feeding
to visualizing results
*tutorial
*tutorial

## Slide 5: 01 FPGA
What is FPGA?
Why should we use it?

## Slide 6
Field Programmable Gate Arrays

## Slide 7: — XILINX
Field Programmable
Gate Arrays
Semiconductor devices based around a matrix of configurable logic blocks (CLBs) connected via programmable interconnects.
Can be reprogrammed to desired application or functionality requirements after manufacturing.
Ref:https://www.electronicdesign.com/technologies/fpgas/article/21801527/the-principles-of-fpgas
Notes: Although one-time programmable (OTP) FPGAs are available, the dominant types are SRAM based which can be reprogrammed as the design evolves.

## Slide 8: FPGA Energy Prototyping Time Various options
Low energy consumption
Fast prototyping
Low time consumption
Easy to integrate with other devices

## Slide 9: FPGA Energy Prototyping Time Various options
Low energy consumption
Fast prototyping
Low time consumption
Easy to integrate with other devices

## Slide 10
LOW
LOW
High
High
Time & Energy Efficiency
Flexibility

## Slide 11: 02 Capsule Colon Endoscopy
About the project

## Slide 12: Capsule Colon Endoscopy
Key Features
low energy consumption
long battery life
stable communication
small size
harmless inside human body

## Slide 13: Capsule Colon Endoscopy
Key Features
low energy consumption
long battery life
stable communication
small size
harmless inside human body
=> processing images before sending to the host can be more efficient.

## Slide 14: 03 AI TRAINING
AI Model Design
Model Training

## Slide 15: Model Design
Input
227*227*3 polyp images
Conv
Conv
Reshape
Output
4*4*3*5
Location of box
& class
ReLU
Max
Pooling
Half
Fire
Max
Pooling
Half
Fire
Max
Pooling
Half
Fire
Half
Fire
Half
Fire
Conv
ReLU
Conv
ReLU

## Slide 16: Model Design
Input
227*227*3 polyp images
Conv
Conv
Reshape
Output
4*4*3*5
Location of box
& class
ReLU
Max
Pooling
Half
Fire
Max
Pooling
Half
Fire
Max
Pooling
Half
Fire
Half
Fire

## Slide 17: Output processing
- 4 X 4 cells on each Image
- 3 Candidates for each cell
- Remove Overlapped Candidates
=> Objectness (Class confidence)
+ Bounding Box

## Slide 18: Can’t show you these images, sorry!

## Slide 19: Binary classification
http://mrl.cs.vsb.cz/eyedataset
0: closed
1: open

## Slide 20: Binary classification
http://mrl.cs.vsb.cz/eyedataset
https://github.com/YooSunYoung/binary_classification_vitis_ai_tutorial
Image Preprocess
        randomly select images
        rescale images into 50X50 gray images
        split images into training and test set
        save images into npy files
        Model
          small model for single class binary classification
Train
  Test
  Freeze
      convert model into protobuf (.pb) format

## Slide 21: Binary classification
http://mrl.cs.vsb.cz/eyedataset
https://github.com/YooSunYoung/binary_classification_vitis_ai_tutorial
Image Preprocess
        randomly select images
        rescale images into 50X50 gray images
        split images into training and test set
        save images into npy files
        Model
          small model for single class binary classification
Train
  Test
  Freeze
      convert model into protobuf (.pb) format
CNN
MAX
POOL
CNN
MAX
POOL
FC
RELU
RELU
RELU
Input
(50x50)
Output
(0 or 1)
Loss: sigmoid_cross_entroy

## Slide 22: 04 ZYNQ Evaluation board Zcu-102
Hardware Information

## Slide 23: Zcu-102
- Evaluation board for FPGA with various peripheral options

## Slide 24: Peripherals
- Evaluation board for FPGA with various peripheral options
A B C D E F
1 2 3 4 5 6

## Slide 25: Peripherals
- Evaluation board for FPGA with various peripheral options
A B C D E F
1 2 3 4 5 6

## Slide 26: Peripherals
- Evaluation board for FPGA with various peripheral options
A B C D E F
1 2 3 4 5 6

## Slide 27: Detail information
- Evaluation board for FPGA with various peripheral options
https://www.xilinx.com/support/documentation/boards_and_kits/zcu102/ug1182-zcu102-eval-bd.pdf
All pheripheral options can be found in the user guide linked below.

## Slide 28: Example application
PC
FPGA
IMGAES
INFERENCE
RESULT

## Slide 29: Zcu-102
SD boot and LAN connection set-up
Boot switch should be set as ↑↓↓↓ before power on

## Slide 30: Zcu-102
Install Petalinux (pre-built) on SD card
Pre-built Peta Linux images:
https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842316/Linux+Prebuilt+Images
How to install linux on SD card:
- Windows: https://www.etcher.net/ *recommend
- Linux: use ‘dd’ command
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18841655/Prepare+Boot+Medium

## Slide 31: Zcu-102
Install Petalinux (pre-built) on SD card
Pre-built Peta Linux images:
https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842316/Linux+Prebuilt+Images
How to install linux on SD card:
- Windows: https://www.etcher.net/ *recommend
- Linux: use ‘dd’ command
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18841655/Prepare+Boot+Medium
UART Connection
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842446/Setup+a+Serial+Console

## Slide 32: Zcu-102
Install Petalinux (pre-built) on SD card
Pre-built Peta Linux images:
https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842316/Linux+Prebuilt+Images
How to install linux on SD card:
- Windows: https://www.etcher.net/ *recommend
- Linux: use ‘dd’ command
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18841655/Prepare+Boot+Medium
UART Connection
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842446/Setup+a+Serial+Console
LAN Connection (Static IP Configuration)

## Slide 33: StatiC IP configuration
ZCU-102 board
PC (Ubuntu)

## Slide 34: StatiC IP configuration
ZCU-102 board
*DNS might need to be configured
PC (Ubuntu)

## Slide 35: StatiC IP configuration
ZCU-102 board
*dns might need to be configured
PC (Ubuntu)

## Slide 36: StatiC IP configuration
ZCU-102 board
PC
PC (Ubuntu)

## Slide 37: StatiC IP configuration
ZCU-102 board
PC (Ubuntu)

## Slide 38: Zcu-102
- Evaluation board for FPGA with various peripheral options
Install Petalinux (pre-built) on SD card
Pre-built Peta Linux images:
https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842316/Linux+Prebuilt+Images
How to install linux on SD card:
- Windows: https://www.etcher.net/ *recommend
- Linux: use ‘dd’ command
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18841655/Prepare+Boot+Medium
UART Connection
Ref: https://xilinx-wiki.atlassian.net/wiki/spaces/A/pages/18842446/Setup+a+Serial+Console
LAN Connection (Static IP Configuration)

## Slide 39: 05 VITIs-AI, AI Implementation
How to implement trained model in FPGA via Vitis-AI

## Slide 40: Hardware programming

## Slide 41: Hardware programming
VHDL

## Slide 42: Hardware programming
VHDL
VERILOG

## Slide 43: Hardware programming
VHDL
VERILOG

## Slide 44: Hardware programming
VHDL
VERILOG

## Slide 45: Hardware programming
VHDL
VERILOG

## Slide 46: VITIs-ai environment set-up

## Slide 47: VITIs-ai environment set-up

## Slide 48: VITIs-ai environment set-up
https://hub.docker.com/r/xilinx/vitis-ai

## Slide 49: VITIs-ai environment set-up
https://hub.docker.com/r/xilinx/vitis-ai
https://github.com/Xilinx/Vitis-AI/tree/master/setup/docker

## Slide 50: VITIs-ai environment set-up
https://github.com/Xilinx/Vitis-AI/tree/master/setup/docker
-v {pwd} /workspace
By default

## Slide 51: VITIs-ai environment set-up
-v {pwd} /workspace
By default

## Slide 52: VITIs-ai environment set-up
-v {pwd} /workspace
By default
In Docker Container
vitis-ai-neptune
vitis-ai-caffe

## Slide 53: VITIs-ai environment set-up
-v {pwd} /workspace
By default
In Docker Container
-> python path

## Slide 54: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Ref: https://beetlebox.org/category/tutorials/
Docker Container
https://github.com/YooSunYoung/binary_classification_vitis_ai_tutorial

## Slide 55: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Environment Setting
Training
Freeze Model
Evaluate Frozen Graph
Quantize
Evaluate Quantized Graph
Compile
Ref: https://beetlebox.org/category/tutorials/
Docker Container

## Slide 56: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Environment Setting
Training
Freeze Model
Evaluate Frozen Graph
Quantize
Evaluate Quantized Graph
Compile
Ref: https://beetlebox.org/category/tutorials/
Docker Container

## Slide 57: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Environment Setting
Training
Freeze Model
Evaluate Frozen Graph
Quantize
Evaluate Quantized Graph
Compile
Ref: https://beetlebox.org/category/tutorials/
Docker Container

## Slide 58: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
/workspace/object_detection/
|-- img
|-- log
|-- output
|-- quantize_results
|-- target
|-- calib_list.txt
|-- compile.sh
|-- input_fn.py
|-- quantize_recipe.sh
`-- model.pb
Ref: https://beetlebox.org/category/tutorials/
Docker Container

## Slide 59: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
/workspace/object_detection/
|-- img : png images for calibration
|-- log : log files
|-- output : output of compiler, DPU executable files
|-- quantize_results : output of quantizer
|-- target : application and DPU executable files
|-- calib_list.txt : list of images for calibration
|-- compile.sh : bash script for compiling
|-- input_fn.py : calibration function for quantization
|-- quantize_recipe.sh : bash script for quantization
`-- model.pb : frozen model
*ls img > calib_list.txt
Ref: https://beetlebox.org/category/tutorials/
Docker Container

## Slide 60: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Quantize
Ref: https://beetlebox.org/category/tutorials/
vai_q_tensorflow quantize \ : vitis-ai command
--input_frozen_graph model.pb \ : frozen model
--input_nodes normalized_gray_image \
--input_shapes ?,50,50,1 \
--output_nodes final_output \
--input_fn input_fn.calib_input \ : input_fn.py
--method 0 \
--gpu 0 \
--calib_iter 30 \
--output_dir ./quantize_results \ : output directory
--weight_bit 8 \ : from 32-bit to 8-bit
--activation_bit 8 \
quantize_recipe.sh
Docker Container

## Slide 61: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Quantize
Ref: https://beetlebox.org/category/tutorials/
vai_q_tensorflow quantize \
--input_frozen_graph model.pb \
--input_nodes normalized_gray_image \
--input_shapes ?,50,50,1 \
--output_nodes final_output \
--input_fn input_fn.calib_input \
--method 0 \
--gpu 0 \
--calib_iter 30 \
--output_dir ./quantize_results \
--weight_bit 8 \
--activation_bit 8 \
quantize_recipe.sh
Already determined in the frozen model
Docker Container

## Slide 62: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Quantize
Ref: https://beetlebox.org/category/tutorials/
quantize_recipe.sh
Docker Container

## Slide 63: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Compile
Ref: https://beetlebox.org/category/tutorials/
compile() {
vai_c_tensorflow \
--frozen_pb ./quantize_results/deploy_model.pb \
--arch /opt/vitis_ai/compiler/arch/DPUCZDX8G/ZCU102/arch.json \
--output_dir ./output/ \
--net_name simple_net \
--options "{'mode':'normal'}"
}
compile | tee ./log/compile_log_zcu102
compile.sh
Docker Container

## Slide 64: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Compile
Ref: https://beetlebox.org/category/tutorials/
compile.sh
Docker Container

## Slide 65: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
File Transfer
Ref: https://beetlebox.org/category/tutorials/
/object_detection/target/
|-- dpuv2_rundir
|-- images
|-- single_image
|-- app.py
|-- compile_so.sh
|-- dpu_simple_net.elf
|-- runner.py
`-- simple_net_kernel_graph.gv
target.tar.gz
Docker Container

## Slide 66: VITIs-ai AI implementation
Image Feeding
PC
https://github.com/YooSunYoung/binary_classification_vitis_ai_tutorial/blob/master/image_feeder.py
Feed images Via Socket Communication

## Slide 67: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Compile
Ref: https://beetlebox.org/category/tutorials/
FPGA Board

## Slide 68: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Runner.py
Ref: https://beetlebox.org/category/tutorials/
FPGA Board
DPU library wrapper

## Slide 69: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Runner.py
Ref: https://beetlebox.org/category/tutorials/
FPGA Board

## Slide 70: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Ref: https://beetlebox.org/category/tutorials/
FPGA Board
Runner.py

## Slide 71: VITIs-ai AI implementation
Ref: https://github.com/Xilinx/Vitis-AI-Tutorials/tree/CIFAR10-Classification-with-TensorFlow
Ref: https://beetlebox.org/category/tutorials/
FPGA Board
App.py
https://github.com/YooSunYoung/binary_classification_vitis_ai_tutorial/blob/master/object_detection/target/app.py

## Slide 72: Demonstration
06

## Slide 73: THANKS!
Do you have any questions?
syo@mmmi.sdu.dk